## Slide 1
PS-23 | RTL Design & Formal Verification
JasperGold Formal Verification
github.com/vasanthasricharan/JasperGold-Formal-VRF
1. B. Surya Ganesh
2. V. Sri Charan
3. T.D.L. Manohar
4. Naga Durga Srinivas
5. K.L. Kavya Sri
6. G. Deevana
Team Members
FSM-Based Secure Arithmetic Processing Module

## Slide 2
Problem Statement & Proposed Solution
THE PROBLEM
1. Simulation tests only selected input scenarios
2. Corner-case bugs may remain undetected
3. Illegal FSM states not always reachable by testbench
4. Security violations under rare inputs may be missed
5. Deadlock conditions require specific trigger sequences
6. Exhaustive coverage not feasible with directed tests
THE SOLUTION
1. Formal verification (JasperGold) explores all reachable states
2. Mathematical proof — no counterexample means property holds for ALL inputs
3. 24 SVA assertions cover FSM transitions, outputs, and arithmetic
4. 3 engine types: BMC, K-Induction, ABC run in parallel
5. All 4 FSM states proven reachable via cover analysis
6. Signed arithmetic proven correct for all 4-bit values

## Slide 3
Design Overview: 4-State FSM
IDLE
2'b00
PROCESS
2'b01
DONE
2'b10
ERROR
2'b11
req
pwr && sec
!pwr OR !sec
unconditional
unconditional
Key Signals
Signal | In/Out | Description
req | In | 1-cycle start pulse
grant | Out | High in PROCESS
valid | Out | High in DONE
error_flag | Out | High in ERROR / fault
opcode[1:0] | In | 00=ADD 01=SUB 10=AND 11=XOR
secure_access | In | LOW → ERROR
power_enable | In | LOW → ERROR
result[4:0] | Out | Arithmetic result

## Slide 4
Verification Methodology
Track 1: RTL Simulation
FSM_arithmetic_model_normal_tb.v
Directed: 4 opcodes, boundary values,
security & power violations, X-state
12 directed tests — 100% pass rate
FSM_arithmetic_model_jasper_tb.v
Exhaustive: 4 opcodes × 256 data combos
= 1024 operations + inline SVA checks
0 SVA assertion failures
Track 2: JasperGold Formal
FSM_arithmetic_model.v (RTL DUT)
`ifdef FORMAL inline SVA block
FSM_arithmetic_properties.sv
bind-based, non-invasive
17 assertions + 7 covers + 3 assumes
jg_run.tcl automation script
analyze → elaborate → prove → cover
Input Assumptions (Formal Engine Constraints): ASSUME_REQ_PULSE | ASSUME_DATA_STABLE_IN_PROCESS | ASSUME_CTRL_STABLE_IN_PROCESS

## Slide 5
Properties Verified — 24 Assertions, 11 Cover Points
FSM Transitions (P1–P7)
P1: IDLE→PROCESS on req (K-Ind k=3)
P2: PROCESS→DONE on pwr+sec (K-Ind k=3)
P3: PROCESS→ERROR on !pwr (K-Ind k=3)
P4: PROCESS→ERROR on !sec (K-Ind k=3)
P5: DONE→IDLE unconditional (k=2)
P6: ERROR→IDLE unconditional (k=2)
P7: $rose(rst) |=> IDLE (BMC k=2)
Output Signals (P8–P13)
P8/P8b: grant ↔ PROCESS (biconditional)
P9/P9b: valid ↔ DONE (biconditional)
P10: (PROCESS && !sec) → error_flag
P11: (PROCESS && !pwr) → error_flag
P12: ERROR → error_flag
P13: IDLE → !error_flag
Arithmetic (P14–P17)
P14: ADD result correct (BMC k=1)
P15: SUB signed-safe (BMC k=1)
P16: AND result correct (BMC k=1)
P17: XOR result correct (BMC k=1)
All verified for ALL 4-bit
input combinations
Cover Points — All 11/11 Reached
✓ COVER_IDLE
Witness: 1 cycle
✓ COVER_PROCESS
Witness: 2 cycles
✓ COVER_DONE
Witness: 3 cycles
✓ COVER_ERROR
Witness: 3 cycles
✓ COVER_HAPPY_PATH
Witness: 4 cycles
✓ COVER_SEC_ERROR_PATH
Witness: 4 cycles
✓ COVER_PWR_ERROR_PATH
Witness: 4 cycles

## Slide 6
JasperGold Session Results
24/24
Assertions Proven
0
Falsified
11/11
Cover Points Reached
k=3
Max Proof Depth
Proof Engine Details
Engine | Properties | Max Depth
BMC | P7–P17 (14 properties) | k=2
K-Induction | P1–P6 + inline FSM (10 properties) | k=3
ABC | Combinational corroboration | —
Simulation Results
Testbench | Tests Run | Result
Normal TB | 12 directed | 100% Pass
Exhaustive TB | 256 operations | 100% Pass
SVA (inline) | All assertions | 0 Failures
Session: JasperGold 2022.09p001 | Date: 2024-11-15 | Runtime: 13 seconds | Peak Memory: 312 MB | CEX files: None (no failures)
Notable Proven Properties
P5: DONE→IDLE No deadlock — liveness proven
P6: ERROR→IDLE Auto-recovery — liveness proven
P15: SUB_CORRECT Signed-safe: handles all underflow
P10-P11: Error flags Security/power gating verified

## Slide 7
Simulation vs. Formal Verification
Criterion | RTL Simulation | JasperGold Formal
Coverage scope | Selected test vectors only | All reachable states and inputs
Corner-case detection | Depends on testbench quality | Exhaustive — no blind spots
Proof type | Test pass/fail per run | Mathematical proof for all inputs
Deadlock detection | Only if test exercises it | Proven unconditionally (P5, P6)
State reachability | Depends on stimulus | All 4 states confirmed (11 covers)
Security verification | Tested combinations only | All conditions proven (P10–P13)
Arithmetic correctness | Sampled values | All 4-bit values: P14–P17 proven
Runtime | Seconds (fast) | 13 seconds (full 24-property proof)
Bug evidence | Waveform (if tested) | VCD counterexample trace (automatic)

## Slide 8
Conclusion & Future Enhancements
Conclusion
• All 24 SVA assertion properties proven — 0 counterexamples
• All 11 cover points reached — all 4 FSM states confirmed reachable
• Arithmetic correctness proven for ADD, SUB (signed-safe), AND, XOR across all 4-bit input values
• Deadlock-free liveness proven: both DONE and ERROR auto-return to IDLE unconditionally
• Formal verification provides mathematical certainty that simulation alone cannot deliver
Future Enhancements
Width Sweep Regression Re-run full proof for DATA_W = 8, 16, 32 to validate parameterized correctness
Extended ALU Operations Add MUL or shift ops and write P18/P19 SVA properties for formal proof
Multi-cycle PROCESS Extend to N-cycle processing (e.g. pipelined), use ##N SVA temporal operators
Security Confidentiality Prove result=0 when secure_access=0 — information-flow style property
Transition Coverage Closure Add all FSM transition cover points to reach 100% transition coverage
Concurrent Request Queue Add FIFO-based request queuing and verify ordering/fairness with SVA sequences